## Slide 1: COEN 146 Computer Networks
Lab7: Link state routing

## Slide 2: Objective
To develop link state (LS) routing algorithm
Routing protocol
Dijkstra's Shortest Path Algorithm

## Slide 3: Link State Routing Protocol
Each Node maintains a connectivity map of all nodes
Updates to other nodes whenever a weight changes

## Slide 4: Dijkstra algorithm
Data:
define N, E, C, and “empty” Nprime arrays
set source node to u
Define D(v) cost of path from source u to dest v
Define p(v) predecessor node along path from u to v
Initialization:
Nprime ← u for each node v in N:
If v adjacent to u
D(v) ← C(u,v)
p(v) ← u
else
D(v) ← INFINITY
D(u) ← 0 // Distance from source to source
Loop: while all nodes not in Nprime:
node ← node in N with min D(node) // node with the least distance neighbor will be selected first remove node from N and add to Nprime update D(v) for all v adjacent to node and not in Nprime
D(v) ← min (D(v), D(node)+C(node, v)(
p(v) ← v (if D(v) is minimum, or node if D(node)+c(node, v) is minimum
Repeat

## Slide 5: Mutex: lock
Used to specify a “critical region” where one thread could access
pthread_mutex_t lock; //declare a lock
pthread_mutex_init(&lock, NULL); //initialize a lock
pthread_mutex_lock(&lock); //acquire/wait for lock
// your code to modify shared variables
pthread_mutex_unlock(&lock); //release the lock

## Slide 6: Input files
Costs
  N*N matrix
  (i, j) represents the cost of link between node i and j
Machines
  Information about the nodes
  Format: <machine_name> <ip_addr> <port_num>

## Slide 7: Threads
receive_info: listen for link state updates from its neighbors
  Update the cost table according
  Message format: <node_id><neighbor_id><new_cost>
run_link_state: loop forever
  Run Dijkstra
  Wait 10-20 seconds after each iteration
user_update (main thread)
  User input update the cost table: <neighbor_id><new_cost>
  Update the cost to all other nodes: <node_id><neighbor_id><new_cost>

## Slide 8: Program structure
The program should be executed as
./executable <process id> <process count> <machines> <costs>
Different process should be executed in different terminals
  Different process have different ids
  Costs and machines file should be the same